## Slide 1
Smart Home Project
Temperature Control
KY-013
GitHub link.com

## Slide 2: The Sensor: KY-013
KY-013
The – pin is Gnd
The Middle pin is Vcc
The S pin is Signal
Datasheet: https://tkkrlab.nl/wiki/Arduino_KY-013_Temperature_sensor_module

## Slide 3: The Relay:
KY-013
The coil pins are for switching the movable contact (COM) between N/O and N/C.
COM is normally connected to N/C.
When current flows in Coil Terminals then the movable contact switch to N/O.

## Slide 4: The Layout of The Design
KY-013

## Slide 5: The Code:
byte temp_sensor_pin = A0; //for the sensor's output pin
float sensor_read; //analog value read from the sensor
double temp_cel; //temperature in celsius
byte fan_pin = 8; //for the fan's enable
byte heater_pin = 9; //for the heater's enable
double Thermistor(float RawADC) { //convert the sensor's read to celcius
double Temp;
Temp = log(10000.0*((1024.0/RawADC-1)));
Temp = 1 / (0.001129148 + (0.000234125 + (0.0000000876741 * Temp * Temp ))* Temp );//Temp in Kelvin
Temp = Temp - 273.15; // Convert Kelvin to Celcius
return Temp;
}
void setup() {
pinMode(fan_pin,OUTPUT);
pinMode(heater_pin,OUTPUT);
Serial.begin(9600);
}
void loop() {
sensor_read = analogRead(temp_sensor_pin);
temp_cel = Thermistor(sensor_read);
if(temp_cel >= 29){ //the range is chosen to satisfy the user's preferences
digitalWrite(fan_pin,HIGH);
digitalWrite(heater_pin,LOW);
}
else if(temp_cel <=23){
digitalWrite(heater_pin,HIGH);
digitalWrite(fan_pin,LOW);
}
else if(temp_cel < 27 && temp_cel > 21){
digitalWrite(heater_pin,LOW);
digitalWrite(fan_pin,LOW);
}
}
KY-013

## Slide 6: How It Works
The sensor contentiously measures the temperature in the room.
When the temperature rises to a predefined level then a fan is switched on.
when the temperature drops top a predefined level the a heater is switched on.
A gray area is added (Schmitt trigger) to prevent oscillation (turning the fan/heater on and off repeatedly in a short time).
A capacitor is added to relay to prevent hardware oscillation.
The temperature at which the fan and heater are switched on should be chosen to satisfy the user’s preferences.
KY-013

## Slide 7: Click to add title
This PowerPoint Template has clean and neutral design that can be adapted to any content and meets various market segments. With this many slides you are able to make a complete PowerPoint Presentation that best suit your needs.
This PowerPoint Template has clean and neutral design that can be adapted to any content and meets various market segments. With this many slides you are able to make a complete PowerPoint Presentation that best suit your needs.
This PowerPoint Template has clean and neutral design that can be adapted to any content and meets various market segments. With this many slides you are able to make a complete PowerPoint Presentation that best suit your needs.
KY-013